## Slide 1: Local FCalPulse Mtg
J.Rutherfoord
4 March 2021
v1

## Slide 2: Outline
PowerPoints from past Local Group Meetings
Status of preamps
Latest on the Sr-90 beta source
Fast trigger
Status of shower calorimeters
Analysis of simulated 350 GeV electrons impinging on our test beam setup

## Slide 3: FCalPulse Local Group Meetings
Powerpoints of the talks of past meetings can be found at http://atlas.physics.arizona.edu/Arizona_Atlas_Downloads/FCalPulse/LocalTalks

## Slide 4: FCalPulse Preamps
Amplifies the calorimeter signals
11 + 11 channels
Designed and built at TRIUMF (Leonid)
New, more robust design
Printed-circuit boards completed
Boards and components at assembly house
Expected to be returned in a week
Another week to test and certify

## Slide 5
New PreAmps
Leonid Kurchaninov
Delivered to TRIUMF
Testing started – will extend into next week
We might receive them late next week or the following week.
Now 11 channels/board
 Need 22 channels in all
More space between channels for better isolation
Improved filtering on low voltage power

## Slide 7: Hot beta source - Status
Manufacturer: IPPE Obninsk
  We asked them to pause production
  Their proposal to enclose the SrCl2 in 100 m of Indium is unacceptable.
    Indium is too dense and Z is too high
    Defeats the point of the thin Titanium shell wall
Source foil
Shell

## Slide 9: Trigger Scintillators
Ready to order scintillator plastic

## Slide 10: Shower Calorimeters on L/R

## Slide 11: W-plate Shower Calorimeters
Purpose
  Develop EM shower which is max at PEEK block
News from IHEP/Protvino (Sergey Denisov)
  Tungsten plates are completed
  Trouble drilling holes for ground pins