## Slide 1: FCalPulse Local Mtg
J.Rutherfoord
1 April 2021
v1

## Slide 2: Outline
New PreAmplifiers
Rob Walker report
  Sticking the Strontium salt to the foil
  Jobs in the shop
Justin Hink and Evan LaForge
  Shower leakage out the sides
Graham - update on “Adding Pulses”

## Slide 3: FCalPulse Readout
A is current measuring device
Schematic of one channel (of 22) of our current measuring devices
Leonid Kurchaninov (TRIUMF) provided
22 preamp channels
16 digitizer channels
Pulser by Giam Jia Hao
HV board by Dan Tompkins
Pink is liquid argon between two electrode plates

## Slide 4: One of 5 boards shown here Each preamp board has 11 channels One channel is in the red box We need two boards Input on the left Output on the right 6 V power at the top
FCalPulse Preamps

## Slide 5
Common emitter with emitter degeneration Low noise.
Common base
Cascode configuration
Good high frequency performance
Emitter follower
Small load on previous stage
Current amplifier
Makes input look like ‘cold’ 50 