## Slide 1: Source Foil R&D Updates
April 1, 2021
Robert Walker

## Slide 2: Updates
Faraday cages have been submitted to the machine shop.
Adhesive R&D continues.
  Elmer’s glue is looking more and more promising.
  More work needs to be done.
Received the foil press parts yesterday.

## Slide 3: Foil Press Received
Surface finish was not satisfactory.
  When assembled could see light between surfaces.
Solution: sand/polish to 2000 grit

## Slide 4: Foil Press continued

## Slide 5: Foil Press continued
  Alignment holes not drilled within spec tolerance.
  One spacer piece undersized.
  Results in a >0.5mm gap in press area.

## Slide 6: What’s Next
Must determine specs of new piece to correct for errors.
Get new spacer piece made.
In the meantime, make temporary fix to existing press to move forward with R&D.
  Glue foil and/or Teflon to fill gap.