## Slide 1: MMFE-8
SolidWorks layout
FPGA

## Slide 2: MMFE-8 PCB

## Slide 3: MMFE_8 w/ FPGA Block Diagram
Artix XC7A200T-2FBG676Cv
VMM 1.2 VDC_Analog
VMM 1.2 VDC_Digital
FPGA 1.8/1.2/1.0 VDC
VMM2_7
SPI CFG
BCnt + Ctrl
TRIG/ADDR: 16
L1 Accept
SPI MOSI to VMM2_1 CONFIG + CLK
64 Sig In
SPI MISO from VMM2
TTC, CTRL, Status Clk
D0, D1, STATUS: 48
L1 Sync, L1 Clk
ACLK
2
VMM2_1
SPI CFG
BCnt + Ctrl
L1 Accept
64 Sig In
Dual Zebra + Protection
ACLK
VMM2_2
SPI CFG
BCnt + Ctrl
L1 Accept
64 Sig In
ACLK
VMM2_3
SPI CFG
BCnt + Ctrl
L1 Accept
64 Sig In
ACLK
VMM2_4
SPI CFG
BCnt + Ctrl
L1 Accept
64 Sig In
ACLK
VMM2_5
SPI CFG
BCnt + Ctrl
L1 Accept
64 Sig In
ACLK
VMM2_6
SPI CFG
BCnt + Ctrl
L1 Accept
64 Sig In
ACLK
VMM2_8
SPI CFG
BCnt + Ctrl
L1 Accept
64 Sig In
ACLK
6
2
6
2
6
2
6
2
6
2
6
2
2
10
8
74
ART Clk
6
6
2
4
Protection
uHDMI
SRS
uHDMI
GbE
miniSAS 8i
24 VDC
GbE
PHY
Config
Flash
uHDMI
GBT
Config
JTAG
Local
OSC
ADC
24

## Slide 4: MMFE-8
Input
  2 x 256 channel Zebra connectors (Ruter Elastomer)
  Compatible with sTGC
  24V Power connector TBD
Input / Output
  JTAG for FPGA Configuration
  ≤ 68pin miniSAS 8i I/O (e-link)
  μHDMI for SRS (still TBD with Sorin)
  μHDMI for future dual GBT or dual e-link
  μHDMI for ethernet

## Slide 5: I/O Connections between FPGA and VMMs
Configuration (3 pairs)
  Configuration clock (potential multidrop)
  di and d0
ART Data (2 pairs)
  ART clock (potential multidrop)
  ART data to ART ASIC
L1 Data (4 pairs)
  L1 Data clock (potential multidrop)
  SYNCH
  L1 Data (d0 and d1)
TTC (5 pairs)
  BC clock (phase adjusted) (potential multidrop)
  L1A (potential multidrop)
  BCR (potential multidrop)
  FER (potential multidrop)
  CAL
Control (2 pairs)
  WEN and ENA
Status (2 pairs)
  VMM status
  Status clock (potential multidrop)
Implies Worst Case
18 x 8 = 144 pairs (288 pins)
for FPGA
Implies Best Case
10 x 8 + 8 - 8 = 88 pairs (160 pins)
for FPGA (pairs + MD – ART)

## Slide 6: Connections between FPGA and MMFE-8 I/O
SRS uHDMI (need Sorin’s input) (4 pairs)
  4 undefined pairs
GbE uHDMI (4 pairs)
  4 pairs from PHY (need magnetics and adapter)
  14 pins to PHY from FPGA
GTB uHDMI (3 pairs)
  2, 3, or 4 pairs depending on application (single, dual, GTB or e-link)
miniSAS 8i (24 pairs)
  Configuration, Control and Status (3 pair e-link)
    Configuration (encoded)
    WEN and ENA (encoded)
    Status (encoded)
  TTC (3 pair e-link)
    BC clock (phase adjusted e-link clk)
    L1A (encoded)
    BCR (encoded)
    FER (encoded)
    CAL (encoded)
    JTAG (encoded)
  L1 Data (3 pair e-link)
  ART data (8 + 1 =9 pairs)
JTAG(4 pins)
sTGC needs? TTP signals are currently left open…
Implies
36 pairs (72 pins)
For FPGA
Implies
18 pairs (36 pins)
For miniSAS 8i

## Slide 7: FPGA Choice

## Slide 8: FPGA Choice

## Slide 9: FPGA Choice

## Slide 10: FPGA Choice
Design files exist for S6 and K7 (Arizona) and A7 (Weizmann)
Vivado can be used with *7 FPGA’s
Zynq has ARM capability (easier testing via C?)
S6 needs fewer voltages
A7, K7, Z7 have ADC capabilities
Chose XC7A200T-2FBG676C
  Best known architecture and tools
  3 rail power solution
  No bank restrictions
  Has MB solution available
  Nearly identical dev board and IP
  Good chance of Rad Hard acceptance
  Comparable cost $250
  Comparable size 729mm
  Comparable power ~600mW quiescent

## Slide 11: FPGA Power Estimate
Xilinx Power Management Solutions Guide from Analog Devices
1V -- ICCINT=3.15A; ICCBRAM=.100A?; IMGT_AVCC=.511A =>3.66A
1.2V -- ICCIO=0.1A; IMGT_AVTT=0.36A; ICCO=.511A => .971A
1.8V – ICCAUX=0.32A
Next: XPE Power Estimation—Use Cases for Artix-7/Kintex-7

## Slide 12: VMM Power Estimate
VMM requires separate Analog 1.2V supply, 8mW/ch * 64 = 512mW => 427mA.
VMM requires separate Digital 1.2V supply, 10mW/pr * 18 = 180mW => 150mA.
8 VMM’s require Ivmma = 3.4A; Ivmmd = 1.2A

## Slide 13: Power Solution
1 x LTM4619
  Drop 24Vin to 1.8Va for Vvmma
  Drop 24Vin to 1.8Vd for Vvmmd
  Use 1.8Vd for 1.8Vfpga
2 x 8 LT3080
  Drop 1.8Va to 1.2Va for Vvmma
  Drop 1.8Vd to 1.2Vd for Vvmmd
  Awaiting Gianluigi’s feedback
1 x LTM4619
  Drop 24Vin to 1.2Vfpga
  Drop 24Vin to 1.0Vfpga
Utilize additional LTM4619 if required.
LTM4619 and LT3080 have successful Rad Hard history.
Use Chip Inductors liberally to separate power inputs, permit direct current measurement.
Use Bulk and Bypass Caps Liberally to reduce supply noise.

## Slide 14: Analog Input Considerations: Impedance
Kapton Thickness | 0.06 | mm | 2.36 | mil |  | 
Er Kapton | 3.4 |  |  |  |  | 
Honeycomb Thickness | 9 | mm | 354.33 | mil |  | 
Er Argon - CO2 | 1 |  |  |  |  | 
Trace Width | 0.3 | mm | 11.81 | mil |  | 
Trace Pitch | 0.45 | mm | 17.72 | mil |  | 
MM Impedance Calc |  |  |  |  |  | 
Single Ended Microstrip |  |  |  | Differential Microstrip |  | 
Target Impedance |  | 13 |  |  | 26 | 26
Model Impedance | 13.12 | 14.04 |  | 26.22 | 28.03 | 24.07
Trace width | 11.81 | 13.50 |  | 11.81 | 13.50 | 11.81
Dielectric Er | 3.4 | 4.3 |  | 3.4 | 4.3 | 4.3
Dielectric height | 2.36 | 3.00 |  | 2.36 | 3.00 | 2.36
Trace thickness | 0.7 | 1.4 |  | 0.7 | 1.4 | 0.7
Differential Spacing |  |  |  | 17.72 | 17.72 | 17.72

## Slide 15: Analog Input Considerations: Protection:
NUP4114 is the current protection device in use.
  ESD Rating for contact is +/- 8 KV
  Capacitance is 1 - 0.3pf
New proposed ESD7008 has:
  Same manufacturer
  Lower capacitance 0.2pf
  Higher ESD Rating for contact +/- 15 KV
  Comparable cost per channel
  Slightly larger packaging (to dissipate energy)
  Bidirectional capability
Testing leakage current now…

## Slide 16: Analog / Digital Design Considerations
Analog Power should not overlap Digital ground planes, and vice versa.
Analog length matching is not important, however impedance matching is.
Digital length and impedance matching is important, within pairs, and within clock domains.
Distributed clocks such as ART to VMM should be the same distance from the FPGA.

## Slide 17: Configuration
Startup FPGA configuration should be stored in the config flash, This will speed up startup.
A Golden config should be kept in flash, to speed recovery.
VMM config should be stored in flash.
Flash can be configured via JTAG.
A serial number can be stored in the flash.

## Slide 18: ADC
ADC is built into the FPGA.
  32 Channels
  12bit
  1MHz
  0-1V
3 ADC lines can be provided to each VMM from the FPGA, for cal and diagnostics.
ADC also monitors Power and Temp.

## Slide 24: Readout of MMFE-8
GbE out
(UDP
packets) to MATLAB
GbE out
(UDP
packets)
4 x MMFE-8,
each containing
8 VMM ASICs
4 x miniSAS
cables (32 ART,
3+ E-Link each)
Custom
S6-FMC
The Virtex 6 contains
transfer logic to configure
and readout the VMM
The Spartan 6 on the S6-FMC
is used to translate voltage
levels to/from VMM
PCIe out
packets to Chassis
Or Versa-
Link
(Custom
packets)

## Slide 25: Readout of MMFE-8
GbE out
(UDP
packets) to MATLAB
GbE out
(UDP
packets)
4 x MMFE-8,
each containing
8 VMM ASICs
4 x miniSAS
cables (32 ART,
3+ E-Link each)
The Virtex 6 contains
transfer logic to configure
and readout the VMM
The Spartan 6 on the S6-FMC
is used to translate voltage
levels to/from VMM
PCIe out
packets to Chassis
Or Versa-
Link
(Custom
packets)